## Slide 1: OpenSAMPL – Timing Measurement and Assurance
June 1-4, 2026 | IEEE SGSMA Santiago, Chile
Joshua N. Grant
ORNL
Notes: This work addresses a fundamental but under-observed problem in power systems: time trust.

## Slide 2: Motivation: Why Time Matters
Time is Critical Infrastructure
Grid operations depend on precise, shared time
Microseconds can determine:
  Stability vs failure
  Accurate vs misleading measurements
Synchronization underpins:
  PMUs
  Protection systems
  Event reconstruction
Notes: Emphasize that time is not just a parameter—it is a dependency layer for everything else

## Slide 3: Fundamental Concept: Clocks are Imperfect
Clocks Always Drift
Every clock has
  Drift (frequency error)
  Offset (time error)
Even synchronized clocks diverge without correction
Influenced by:
  Temperature
  Hardware aging
  Network conditions
Notes: Sets up inevitability of error → need for monitoring

## Slide 4: The Real-World Problem
Modern Timing Systems Are Fragile
GNSS dependency is vulnerable:
  Jamming
  Spoofing
Networking timing (PTP):
  Packet delay variation
  Asymmetry
Oscillator holdover drift can accumulate quickly
Notes: Emphasize: systems are precise but brittle

## Slide 5: Operational Challenges
Notes: This slide transitions from physics to operations

## Slide 6: Accuracy ≠ Assurance

## Slide 7: The Gap: No Continuous Timing Assurance

## Slide 8: Introducing OpenSAMPL
Open-source Python framework
Unified platform for:
  Ingesting timing data
  Analyzing synchronization
  Visualizing system health
Vendor agnostic
Notes: OpenSAMPL provides observability for time.

## Slide 9: OpenSAMPL Architecture

## Slide 10: Standardized Data Ingestion
Customizable Near Real-Time Data Collection
Supports
  GNSS clocks
  PTP devices
Interfaces:
  APIs
  SNMP
  File Ingestion
Extensible via plugins
PTP
Oscillator
NTP
Standardized Data Format

## Slide 11: Synthetic Data Capability

## Slide 12: Analytics & Alerting
Time Anomaly Detection
Powered by Grafana
Detect:
  Offset thresholds
  Drift rates
  Cross-device divergence
Continuous monitoring of:
  Clock health
  Synchronization integrity

## Slide 13: Visualization & Situational Awareness
Time-series plots
Geospatial mapping of clocks
Real-time alerts

## Slide 14: Key Design Principles

## Slide 15: Example Scenario
Example: Detecting GNSS Degradation
Multiple substations show:
  Reduced signal quality
  Increasing drift
OpenSAMPL:
  Flags anomaly
  Triggers alerts
  Enables action

## Slide 16: Impact

## Slide 17: Limitations & Challenges

## Slide 18: Future Work and Directions

## Slide 19: Conclusion
Timing is mission-critical
Accuracy alone is insufficient
OpenSAMPL enables:
  Observability
  Assurance
  Action
https://github.com/ORNL/OpenSAMPL
https://pypi.org/project/opensampl/
https://ornl.github.io/OpenSAMPL/